## Slide 1: Quad-copter control center for iOS
By: Joe Ippolite

## Slide 2: Outline
Background
Devices
Software
Demo
Code Review

## Slide 3: Background
Current Senior Design Project
  Controls over same Wi-Fi network
  Limited range
  Need to know IP of quadcopter

## Slide 4: Proposed Solution
Intermediate server
  No need to know IP of quad
  Access from everywhere
  Nearly infinite range
Needs internet access

## Slide 5: Devices Used
3D-Robotics Quad-Copter
  APM(Ardu Pilot Manager)
    Controls Rotors
Raspberry Pi (model B)
  IOIO OTG microcontroller
  Wifi Module
    Replace with GSM module for portability*
iOS Device
  Needs internet connection

## Slide 6: Server Overview
Websocket integration
  On connect unique “Key” given
  On “Add” controllable device added to list of devices
  On Message PWM duty cycles sent to appropriate device
    I.E. “Key” ch1 ch2 ch3 ch4 ch5
  On disconnect removes “Key” from list of devices

## Slide 7: Raspberry Pi
Java program
  Opens websocket connection to server
    “Adds” itself to list of controllable devices
    On message
      Checks for all 5 channel inputs
      Sends corresponding duty cycle to IOIO OTG
IOIO OTG
  Sets PWM duty cycle of 5 GPIO pins
    Pins are connected to APM
Acts as replacement RF receiver

## Slide 8: Pitfalls
Possible delay
Server being overworked
Lack of video feed
GPS not being recorded
  Currently based off of IP location

## Slide 9: Demo

## Slide 10: Code Review